## Slide 1: ELECTRONIC CUBE
Juan Carlos Rodríguez Tallón, Gabriel González Rial
ELECTRONIC LAB PROJECT

## Slide 2: Introduction
Objective
  Electronic cube based on Xiaomi AQara
Wireless
Commercial use  Home automation
Own use  Web server and monitoring

## Slide 3: Components
Other components:
Resistors 68, 1k, 4.7k, 12k
Capacitors 10nF, 2.2nF, 100nF, 10uF, 47uF
Components | Manufacturer | Units | Price (€) | Description
FT232RL-REEL | FTDI | 1 | 3,76 | USB – UART converter
ESP8266-12-E | AI Thinker | 1 | 1 | WiFi Module
MPU-6050 | Invensense | 1 | 7 | Accelerometer/Gyroscope
BC846BWT1G | ON Semiconductor | 5 | 0,6 | General purpose bipolar NPN
NCP1117ST33T3G | ON Semiconductor | 5 | 1,82 | 3,3 V regulator
KM-23ID-F | Kingbright | 15 | 2,06 | LED
MCABT-408-RC | Multicomp | 1 | 0,97 | Buzzer
FSM2JSMASTR | TE Connectivity | 5 | 0,92 | Buttons
PMEG3020DEP | Nexperia | 5 | 1,76 | Schottky diodes
ZX62RD-AB-5P8(30) | Molex | 2 | 0,778 | Micro USB connector
TOTAL COMPONENTS: 23,83 €
TOTAL PCB: 19,24 €

## Slide 4: Components
ESP8266-12-E
MPU-6050

## Slide 5: Schematic. UART & Power
MOSFET (n in parallel)

## Slide 6: Schematic. ESP 8266-12E

## Slide 7: Schematic. MPU6050

## Slide 8: Layout. Distribution

## Slide 9: Layout. Routing

## Slide 10: Validation & Test. PCB
Power 5V-3,3V
USB-UART
Programming Interface
WIFI Interface
LEDs
Buzzer and PWM
I2C
  MPU6050
  OLED Screen

## Slide 11: UART
Inverted UART signals
Fixed using R1,R2 Pads

## Slide 12: MPU6050
No I2C response after soldering
Aliexpress…¯\_(ツ)_/¯
We left other interface
Use comertial module gy-521

## Slide 13: Unitary Tests
Web Interface to deploy Unitary Tests
HTTP Server
Port 80
Toggle Led
Scan I2C Bus
Buzzer
Test Screen
Accelerometer Data

## Slide 14: Performance
Continous accelerometer data on screen.
Enclosure for portable function

## Slide 15: Conclusions
All functionalities work as expected
  Minors flaws in design easible fixable
Always use trusted distributors
  Isolate posible error sources
The Project is considered a success

## Slide 16: Future Work
WiFi Mesh for Domotics

## Slide 17: THANK YOU FOR YOUR ATTENTION